## Slide 1: FPGAs – Part 2: Interconnects and hardwired resources
CE233(CAD), Lecture 6:
Mehdi Modarressi
Department of Electrical and Computer Engineering,
University of Tehran

## Slide 2
Reading:
  Spartan-3 Generation FPGA User Guide, Xilinx ug331 (v1.8)
  “FPGA Prototyping By VHDL Examples- Xilinx Spartan-3 Version”, Chapter 2
  “The Design Warrior's Guide to FPGAs”, Chapter 4

## Slide 3: FPGA interconnects

## Slide 4
How to connect CLB to wires?
Solution: connection box
  Device that allows inputs and outputs of CLB to connect to different wires
CLB
CLB
Connection box
FPGA interconnects- connection box

## Slide 5: Connection box
Connection box characteristics
  Topology
    Defines the specific wires each CLB I/O can connect to
    Examples: same flexibility, different topology
CLB
CLB
CLB
CLB

## Slide 6: FPGA interconnects- switch box
Fs = 3, the most common switch
Low flexibility, good size
Fs = n-1=6: too big but very flexible
Switch Blocks connect horizontal and vertical channels
A trade-off between flexibility and switch size

## Slide 7
Fs=3, why?
XC4000 interconnects

## Slide 8: Switch Matrix Operation
6 pass transistors per switch matrix interconnect point
Pass transistors act as programmable switches
Pass transistor gates are driven by configuration memory cells
After Programming
Before Programming

## Slide 9: FPGA interconnects
Connect Logic Blocks using wires and Programmable Switches

## Slide 10: Digital design flow for FPGAs
VHDL
…..
…..
…..
Logic synthesis
Design entry
Partitioning
Placement
Routing
Physical Design (Layout Synthesis)

## Slide 11: Example
Determine the configuration bits for the following circuit implementation in a 2x2 FPGA, with I/O constraints as shown in the following figure. Assume 2-input LUTs in each CLB.

## Slide 12: CLB structure
Determine the configuration bits for the following circuit implementation in a 2x2 FPGA, with I/O constraints as shown in the following figure. Assume 2-input LUTs in each CLB.

## Slide 13: Switch box structure
Slides taken from Antonio R. Miele Marco D. Santambrogio Politecnico di Milano

## Slide 14: CLBs configuration

## Slide 15: Placement: Select CLBs
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 16: Routing: Select path
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 17: Configuration Bitstream
The configuration bitstream must include ALL CLBs and SBs, even unused ones
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 18: FPGA configuration
The bit-stream is loaded into the FPGA serially through some special input pins

## Slide 19: FPGA configuration
All of the SRAM configuration cells as comprising a long shift register.

## Slide 20: SRAM-based FPGAs
A reasonably high-end device could easily contain 25 million such cells!
Solution: group flip-flops into shorter—say 1,024— shift registers
This group is called a frame.
special-purpose internal circuitry automatically parallel copies/loads this data into the frames

## Slide 21: Routing Architecture
Propagation delay through the routing is a major factor in FPGA performance.
After routing an FPGA, the exact segments and switches used to establish the net are known and the delay from the driving output to each input can be computed.
Any programmable switch (EPROM, pass-transistor, or antifuse) has a significant resistance and capacitance. Each time a signal passes through a programmable switch, another RC stage is added to the propagation delay.

## Slide 22: Routing Architecture
For a fixed R and C, the propagation delay mounts quadratically with the number of series RC stages.
The use of a low resistance switch, such as antifuse, keeps the delay low and its distribution tight.
Of equal significance is optimization of the routing architecture.

## Slide 23: FPGA interconnects- wires
Typically, an FPGA contains a mix of segment lengths:
  Some wires that span only one logic block
  Some wires that span more than one logic block
  Some wires that span the whole chip
If a segment is too short, must traverse many segments to reach your destination
  If a segment is too long, waste routing capacity, extra capacitance: too slow!

## Slide 24: FPGA interconnects- wires
Short segments are good for local connections
Long segments are good for global connections
Most FPGA’s have a variety of segment lengths

## Slide 25: Long wires

## Slide 26: Interconnects in modern FPGAs
Example: Artix-7
Connections between CLBs and other resources use the fabric routing resources
Routes connect resources vertically, horizontally, and diagonally
Wires have different lengths Horizontal: Single, Dual, Quad, Long (12)
  Vertical: Single, Dual, Hex, Long (18)
  Diagonal: Single, Dual, Hex
Notes: Routing decisions are made by the implementation tools, based upon the timing constraints that have been applied to the design.
The lengths of the vertical and diagonal routing resources has increased from the Virtex-6 family to improve vertical routing capabilities:
Quad lines have become Hex lines.
Long lines have increased from 16 to 18.
The changes in the routing lengths also contribute to substantially improved routability.

## Slide 27: Programming technology
Must use a programmable technology to implement the reconfigurable parts
D7
D6
D5
D4
D3
D2
D1
D0
A2
A1
A0
A
B
C
F0
F1
F2
F3
X
X
X
X
X
X
X
X
X
X

## Slide 28: Programmable parts
PAL and PLA connection points
Multiplexers
Interconnects among different components in a programmable chip
Lookup table entries
 These parts will be introduced soon!

## Slide 29: Programming technologies
How the programmable parts are constructed
Three major technologies
  SRAM+ transistor switches
  ROM
  Antifuse

## Slide 30: Programming technology- SRAM
Recall the transistor functionality as a switch

## Slide 31: Programming technology- SRAM
The switch should be controlled by some memory element
  To keep the configuration
A Static Random Access Memory (SRAM) is used
  Each switch is a pass transistor controlled by the state of an SRAM bit
  Needs to be configured at power-on
SRAM Bit 0
SRAM Bit 1

## Slide 32: Programming technology- ROM
Flash Erasable Programmable ROM (Flash)
  Device itself holds the program
  Reprogrammable, even in-circuit
  The configuration is kept, even if the circuit is shut down
32
Wire
Wire

## Slide 33: Programming technology- ROM
ROM: a transistor switch has and additional floating-gate
  Can be turned off by injecting negative charge onto the floating gate: negative charge prevent channel formation
  Can be turned on by discharging the floating gate
EPROM: discharging by UV light
EEPROM: discharging by electrical voltage

## Slide 34: Programming technology- Antifuse
Fusible Links (“Antifuse”)
  Forms a low resistance path when electrically programmed
Lower area and higher speed than SRAM and ROM
Once the fuse is programmed, the state never changes
  One-time programmable
Antifuse
Wire
Wire

## Slide 35: FPGA market
Several companies produce FPGAs and CPLDs
Two major companies: Altera (Intel) and Xilinx