## Slide 1: FSM and FSMD
Mehdi Modarressi
Department of Electrical and Computer Engineering,
University of Tehran
ECE381(CAD), Lecture 8:
Some pictures and examples are taken from “FPGA Prototyping By VHDL Examples- Xilinx Spartan-3 Version”

## Slide 2: FSM and FSMD
Reading:
  “FPGA Prototyping By VHDL Examples- Xilinx Spartan-3 Version”, Chapters 5 and 6

## Slide 3: Introduction
FSM (finite state machine)
FSMD (finite state machine with datapath)
Some design examples
  Pipeline
  Bus
  Debouncer
  ….

## Slide 4: Datapath and control path
Each digital circuit is composed of two parts
  Control path
  Data path
Datapath is the functional units that implement the computation or required operations and services
  Like ALU in a CPU
Control path controls the behavior of the functional units
  Activating datapath components, feeding data to them,…

## Slide 5: FSM
Control path operation: Examines the external commands and also the current status of the system and activates proper control signals to control operation of a datapath
FSMs are used to describe the control path of a digital circuit

## Slide 6: FSM
Moore: the output is only a function of state
Mealy : the output is a function of state and external input

## Slide 7: FSM representation
An FSM is usually specified by a state diagram
A state diagram is composed of nodes, which represent states and are drawn as circles, and annotated transitional arcs

## Slide 8: FSM modeling by VHDL
Example from “The designers guide to VHDL”, page 110
An FSM with both Mealy and Moore outputs

## Slide 9: FSM modeling by VHDL
Use the VHDL‘s enumerated data type to represent the FSM’s states
3-process coding method
  Use one process for state transition, one for next state calculation, and one for output generation

## Slide 10: FSM modeling by VHDL

## Slide 11: PROCESS-1: State transition

## Slide 12: PROCESS-2: State calculation

## Slide 13: PROCESS-3: Output generation

## Slide 15: Example- Rising-edge detector
Moore Mealy
The zero and one states indicate that the input
signal has been ’0’ and ’ 1’ for awhile

## Slide 16: Exercise
Design an FSM with two input signals a and b, and 4 output signals P_in, P_out, C_in, C_out that assert one clock signal when a pedestrian enters, a pedestrian exits, a car enters, and a car exits, respectively.
Implement the FSM by VHDL

## Slide 17: FSMD
Finite state machine with datapath
Combines an FSM and regular sequential circuits

## Slide 18: RTL
The FSMD is used to implement systems described at the Register Transfer Level (RTL)
An RT operation specifies data manipulation and transfer for a single destination register
rdest  f(rsrc1, rsrc2,…,rsrcn)
Elementary operations - called microoperations
  load, count, shift, add, bitwise "OR", etc.
  Example:
    R0 R1  R2
    R6 R7+R8-1

## Slide 19: RT description methodology
Arrow (): data transfer
  e.g. R1  R2
Brackets [ ]: Specifies a memory address
  e.g. R0  M[AR]
Comma: separates parallel operations
Colon: states a condition
  K1: (R2  R1)
  Means:
  If (K1 =1) then (R2  R1)

## Slide 20: RTL
RT operations are synchronized by an embedded clock
The result from the f (.) function is not stored to the destination register until the next rising edge of the clock
a  a-b+l

## Slide 21: RTL
A circuit based on the RT methodology specifies which RT operations should be executed in each step
An RT operation is done in a clock-by-clock basis
  Its timing is similar to a state transition of an FSM

## Slide 22: ASM chart
ASM: algorithmic state machine
Composed of a network of ASM blocks
  State blocks: represents a state in an FSM
  Decision blocks: tests the input condition and determines which exit path to take

## Slide 23: Elements of ASM chart

## Slide 24: State box
The symbol is a rectangle, with a label (state name) and output control operations(Moore type) written inside
It has a single exit path (arrow)

## Slide 25: Decision box
The symbol is a diamond
A condition variable and multiple exit paths, labeled with values of the input condition
It has a single entry path.

## Slide 26: Conditional output box
The symbol is a rounded rectangle
Denotes output signals that are of the Mealy type.
Always after a decision box
Single entry and exit path

## Slide 27: ASMD chart
ASM with datapath
A clock is embedded in the chart
  Registers are updated when exiting the current ASMD block

## Slide 28: ASMD chart

## Slide 29: ASM block
ASM block

## Slide 30: ASMD timing
Control passes one branch in the ASM block during the clock period and waits for the clock to enter the next state box

## Slide 31: ASMD timing
The destination registers are updated when exiting the current ASMD block, but not within the block
  May introduce errors when a register is used in a decision box
If the new value of r is desired, we should use r_next, the output of the combinational logic
“ := “ is used for
immediate assignment

## Slide 32: State diagram- ASM equivalence
Source: EE 459/500 – HDL Based Digital Design with Programmable Logic

## Slide 33: State diagram- ASM equivalence
Source: EE 459/500 – HDL Based Digital Design with Programmable Logic

## Slide 34: ASMD chart

## Slide 35: Example: Fibonacci number
Fibonacci number circuit
A sequence of integers

## Slide 36: ASMD
tl and t0 are temporary storage registers
n is the index register
Input:
  i: the number of required iterations
  Start: Commands the beginning of operation
Output:
  F: the last generated number
  Ready: indicates that the circuit is idle and ready to take new input
  done-tick: asserted for one clock cycle when the operation is completed

## Slide 37: VHDL code

## Slide 38: VHDL code
We use a 3-process implementation, much like the FSM implementation in previous lecture
  but we should also handle the datapath registers in the next state calculation and assignment processes
Process 1: State and datapath register assignment

## Slide 39
Process 2: next state and datapath register
Process 3: output generation, we actually use a dataflow assignment, as the output is very simple