## Slide 1: Verilog Synthesis
Mehdi Modarressi
CE233(CAD), Lecture 10:

## Slide 2: Verilog Synthesis
Learn
  How to write synthesizable Verilog code
  Common mistakes and how to avoid them
  What is synthesized for what we code

## Slide 3: Logic synthesis
Is done automatically by synthesis tools (a.k.a. “silicon compilers”)
Synthesis tools process the HDL then
  Infer logic and memory elements
  Perform technology-independent and technology-dependent optimizations
  Map elements to the target technology

## Slide 4: Logic Synthesis
module x (a,b,c)
….
Always@ (clk)
….
assign a=b &c;
……..
endmodule;
Logic synthesis
In this lecture, we discuss logic synthesis

## Slide 5: Synthesis- Partitioning
partitioning
Gate-level description
Technology Library (Target FPGA)
(just 2-input and 3-input LUTs)
Partitioned circuit

## Slide 6: Placement: Select CLBs
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 7: Routing: Select path
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 8: Configuration Bitstream
The configuration bitstream must include ALL CLBs and SBs, even unused ones
CLB0: 00011
CLB1: ?????
CLB2: 01100
CLB3: XXXXX
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 9: Digital Design Flow - ASIC
2. Simulation &
Functional verification
1. HDL Coding
3. Logic Synthesis
5. Physical Synthesis
4. Simulation &Timing Analysis

## Slide 10: Digital Design Flow - Synthesis

## Slide 11: Synthesis is Constraint-Driven
The designer guides the synthesis tool by providing design constraints:
  Timing requirements (max. expected clock frequency)
  Area requirements
  Maximum power consumption
The synthesis tool uses this constraints and tries to generate the smallest possible design that will satisfy the requirements
Without any constraints specified, the synthesis tool will generate a non-optimal netlist, which might not satisfy the designer’s requirements

## Slide 12: Synthesis tool: (RTL & Logic Synthesis)
Input:
  HDL Code
  “Technology library” file
    Standard cells (known by transistor size, 90nm)
      Basic gates (AND, OR, NOR, …)
      Macro cells (Adders, Muxes, Memory, Flip-flops, …)
  Constraint file (Timing, area, power, optimization Alg.)
Output:
  A gate-level “Netlist” of the design
  Timing files (.sdf)

## Slide 13: Commercial Synthesis Tools
Vendor Name | Tool Name | Target platform
Intel (Altera) | Quartus | FPGA
Xilinx | ISE/ Vivado | FPGA
Mentor Graphics | Precision | FPGA
Synplicity | Synplify | ASIC
Synopsys | Design Compiler | ASIC
Cadence | Ambit | ASIC

## Slide 14: Logic Synthesis
Behavioral coding used to be used for rapid prototyping
  Now, we can get hardware out of it by synthesis tools
Assembly coding vs. C/Java programming
Gate-level modeling vs. behavioral modeling

## Slide 15: Verilog Lower Abstraction Levels
Gate-level:
  All gate-level codes are synthesizable
Dataflow Models:
  Most expressions synthesizable
    Exceptions: *, /, %
  General rule: Delays are all ignored

## Slide 16: Synthesis basics
Hardware Inference
  The specific coding style suggested by tool designers
  e.g. how to make FF
General rules
  Natural mapping of code structures to logic

## Slide 17: Synthesizable Constructs
Not all Verilog constructs are synthesizable because:
  Does not make sense in hardware (e.g. $display, initial block )
  Not possible to achieve (e.g. delay control like #10)
  Not support by design flow
  Too difficult or too abstract for the synthesis software (e.g. A / B)
Synthesizable Constructs
• Ports (input, output, inout)
• Parameter
• module
• wire, reg, tri
• function, task
• always, if, else, case
• assign
• for, while

## Slide 18: Non-Synthesizable Constructs
Non- Synthesizable Constructs
  Initial (used only in testbenches)
  real (real type data type)
  time (time data type)
  comparison to X and Z are ignored (e.g., a == 1’bz)
  delays “#” are ignored by synthesis tools as if it is not there
  The use of Z value
  * and / are synthesizable, but it can be resource-intensive and slow
Some result in error, some are simply ignored

## Slide 19: Behavioral Synthesis
Sometimes not synthesizable, or undesirably synthesized
  Unless rules obeyed
initial statements:
  All ignored
  Use explicit reset signals instead
always statements
  Sensitivity list decides what is synthesized
    Combinational circuits: all variables/ports read in the block
    Sequential circuits: posedge or negedge of the clock

## Slide 20: Synthesis: Combinational Logic
Combination logic function can be expressed as:
logic_output(t) = f(logic_inputs(t))
In case of using always statement, all ports should be listed in the sensitivity list
The combinational logic must not have feedback
Specify the output of a combinational behavior for all possible cases of its inputs
Logic that is not combinational will be synthesized as sequential
Combinational
Logic
logic_inputs(t)
logic_outputs(t)

## Slide 21: Synthesis of Combinational Logic
There are many ways to describe combinational logic with the Verilog HDL, but some are not supported by synthesis tools.
Synthesizable combinational logic can be described by
  a netlist of structural primitives.
  a set of continuous-assignment statements,
  a level-sensitive behavior

## Slide 22: Netlist of primitives
schematic for a netlist of primitives and the circuit synthesized from the netlist

## Slide 23: Continuous Assignment

## Slide 24: Procedural Assignment with always
Procedural assignment allows an alternative, often higher-level, behavioral description of combinational logic
Supports richer, C-like control structures such as if, for, while, case

## Slide 25: Mix-and-Match Assignments
Procedural and continuous assignments can (and often do) co-exist within a module
Procedural assignments update the value of reg. The value will remain unchanged till procedural assignment updates the variable.
This is the main difference with continuous assignments in which the right hand expression is constantly placed on the left-side
continuous assignments
procedural assignments

## Slide 26: Combinational Circuits
always @ (a or b or c)
z= (a & b) | c;

## Slide 27: Combinational Circuits
If a, b, c, and out are 2-bit vectors [1:0], then the above assign statement will translate to two identical circuits for each bit

## Slide 28: If statement
If there is a multiplexer in the library, then use it
Otherwise, use simple gates

## Slide 29: Tri-state Gates
module test(out, i1, i2);
output out;
input i1, i2;
reg out;
always @(i1 or i2)
if (i1)
out = 1'bz;
else
out = i2;
endmodule

## Slide 30: Combinational Circuits
Example: 4-bit adder:
  Used FA blocks if there is in the library
  Otherwise use gates to build it
module test(out, i1, i2);
output [3:0] out;
input [3:0] i1, i2;
reg [3:0] out;
always @(i1 or i2)
out = i1 + i2;
enddmodule

## Slide 31: case Statement
sel[1:0]
a[3:0]
y[3:0]
b[3:0]
c[3:0]
d[3:0]
  module mux_4bits (y, a, b, c, d, sel);
  input [3:0] a, b, c, d;
  input [1:0] sel
  output [3:0] y;
  reg [3:0] y;
  always @ (a or b or c or d or sel)
  case (sel)
  0: y = a;
  1: y = b;
  2: y = c;
  3: y = d;
  default: y = 4'bx;
  endcase
  endmodule

## Slide 32: case Statement
module test(out, i1, i2, i3);
output out;
input [1:0] i1;
input i2, i3;
reg out;
always @(i1 or i2 or i3)
case(i1)
2'b00:out = i2 + i3;
2'b01:out = i2 -i3;
2'b10:out = i2 & i3;
2'b11:out = i2 ^ i3;
endcase
endmodule

## Slide 33: loop Statements
module test(out, i1, i2);
output out;
input [1:0] i1;
input [1:0] i2;
reg [1:0] out;
integer k;
always @(i1 or i2)
for(k=0; k<2; k=k+1)
out[k] = i1[k] & i2[k];
endmodule
Loop replicates the hardware
The loop boundaries must be known at synthesis time

## Slide 34: Encoder
Nested IF-ELSE might lead to an encoder
  Example: 4-to-2 encoder

## Slide 35: Priority Decoder
A case statement may result in a priority decoder

## Slide 36: Bus - concatenation

## Slide 37: Bus - replication

## Slide 38: Comparator

## Slide 39: Logic Optimization
Use parenthesis
Most synthesis tools do this optimization

## Slide 40: Logic optimization- Resource Sharing
Resource sharing: Sharing an operator under mutually exclusive conditions.

## Slide 41: Synthesis: Sequential Logic
General Rule: A variable will be synthesized as a flip-flop when its value is assigned synchronously with an edge of a signal

## Slide 42: Sequential Logic- Flip-Flop
A simple FF

## Slide 43: Sequential Logic- Flip-Flop

## Slide 44: Registered Combinational Logic
Combinational logic that is included in a synchronous behavior will be synthesized with registered output.
Example:
module mux_reg (a, b, c, d, y, select, clock);
  input [7:0] a, b, c, d;
  output [7:0] y;
  input [1:0] select;
  reg [7:0] y;
  always @ (posedge clock)
  case (select)
  0: y <= a; // non-blocking
  1: y <= b; // same result with =
  2: y <= c;
  3: y <= d;
  default y <= 8'bx;
  endcase
  endmodule

## Slide 45: Sequential Logic- latch
If Q were simply a combinational function of D: combinational logic
But are times when the always block executes but Q isn’t assigned (e.g., when G = 0)
The synthesizer has to arrange to remember the value of “old” value Q even if D is changing
→ it will infer the need for a storage element: latch

## Slide 46: Unwanted Latches
module test(out, i1, i2);
output out;
input i1;
input i2;
reg out;
always @(i1 or i2)
if(i1)
out = i2;
endmodule
Latches in this case maybe unwanted
  We used combinational coding rules but a memory element is used

## Slide 47: Unwanted Latches (cont.)
Unintentional latches also result from incomplete case statement
Example: case statement
  always @ (sel_a or sel_b or data_a or data_b)
  case ({sel_a, sel_b})
  2'b10: y_out = data_a;
  2'b01: y_out = data_b;
  endcase
The latch is enabled by the "event or" of the cases under which assignment is explicitly made. e.g. ({sel_a, sel_b} == 2'b10) or ({sel_a, sel_b} == 2'b01)

## Slide 48: Unwanted Latches (cont.)
Example: if .. else statement
  always @ (sel_a or sel_b or data_a or data_b)
  if ({sel_a, sel_b} == 2’b10)
  y_out = data_a;
  else if ({sel_a, sel_b} == 2’b01)
  y_out = data_b;

## Slide 49: Non-blocking Shift Register
Use blocking assignments for combinational logic, and non-blocking assignment for sequential logic
Example: shift register
  always @ (posedge clock) begin
  if (reset == 1'b1) begin
  reg_a <= 1'b0;
  reg_b <= 1'b0;
  reg_c <= 1'b0;
  reg_d <= 1'b0;
  end
  else begin
  reg_a <= Shift_in;
  reg_b <= reg_a;
  reg_c <= reg_b;
  reg_d <= reg_c;
  end
  end

## Slide 50: Synthesis Tip
In general, the event-control expression of a cyclic behavior describing sequential logic must be synchronized to a single edge (posedge or negedge, but not both) of a single clock (synchronizing signal).

## Slide 51: Clock, Reset, Combinational Feedback

## Slide 52: Avoid Combinational Feedback