## Slide 1: Synthesis- Timing Issues
CE233(CAD), Lecture 11:
Mehdi Modarressi
Department of Electrical and Computer Engineering,
University of Tehran

## Slide 2: Timing of digital circuits
Timing: Setup Time and Hold Time Constraints
D
Q
Q’
CLK

## Slide 3: Timing of digital circuits
A typical sequential network has both a combinational circuit and flip-flips.
CLK
CLK
A
B
C
D
Combinational

## Slide 4: Important Timing Parameters

## Slide 5: Timing of digital circuits
CLK
CLK
A
B
C
D
Combinational
tcq + tcomb + tsetup < T
thold < tcq + tcomb
Clock period
Shortest path

## Slide 6: Input Timing Constraints
Setup time: tsetup = time before the clock edge that data must be stable (i.e. not changing)
Hold time: thold = time after the clock edge that data must be stable
Aperture time: ta = time around clock edge that data must be stable (ta = tsetup + thold)

## Slide 7: Output Timing Constraints
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)

## Slide 8: Dynamic Discipline
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements

## Slide 9: Setup Time Constraint
The setup time constraint depends on the maximum delay from register R1 through the combinational logic.
The input to register R2 must be stable at least tsetup before the clock edge.
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)

## Slide 10: Setup time slack
The circuit provides setup time as a function of the clock period, Tpcq and Tpd
The FF requires a specified Tsetup to operate correctly.
The difference between the two is called setup time slack.
setup time slack = (provided setup time) - (required setup time)
We always want positive slack.

## Slide 11: Setup time slack
example

## Slide 12: Hold time
Hold time is the amount of time that FF0’s old data must persist at the input of FF1 after the clock edge

## Slide 13: Hold Time Constraint
The hold time constraint depends on the minimum delay from register R1 through the combinational logic.
The input to register R2 must be stable for at least thold after the clock edge.
thold < tccq + tcd
tcd > thold - tccq

## Slide 14: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps (for each gate)
tcd = 25 ps (for each gate)
tpd =? (for whole circuit)
tcd =? (for whole circuit)
Setup time constraint:
Tc ≥ ?
fc = 1/Tc = ?
Hold time constraint:
tccq + tcd > thold ?

## Slide 15: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!

## Slide 16: Fixing Hold Time Violation
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd =
tcd =
Setup time constraint:
Tc ≥
fc =
Hold time constraint:
tccq + tcd > thold ?
Add buffers to the short paths:

## Slide 17: Fixing Hold Time Violation
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Add buffers to the short paths:

## Slide 18: Clock Skew
The clock doesn’t arrive at all registers at the same time
Skew is the difference between two clock edges
Examine the worst case to guarantee that the dynamic discipline is not violated for any register – many registers in a system!

## Slide 19: Setup Time Constraint with Clock Skew
In the worst case, the CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)

## Slide 20: Hold Time Constraint with Clock Skew
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq